## Slide 1
Servo Recorder Player – System Block Diagram
Orig. 7/19/14 BTL (Lightman) Updated 9/15/14 Rev 4
SD
Card
Audio
(Not Used)
USB
Interface
(Programming)
7.5 VDC*
Notes:
*7.5 VDC covers all power needs except servos.
Separate Servo Power Supply required; Remove jumpers & attach servo power to center pin
Propeller loads program from EEPROM upon power up; IDE can download program
SD Card contains 2 files 1) Servo Commands, 2) Profile for Servos
Pots can be reversed by switching 5V and Gnd lines to pots
Servo Cables contain Signal, +5V, Gnd
Propeller Activity Board
SD Card Contains:
Servo Commands
Profile for Servos
Pot D
(ADC 0)
Pot C
(ADC 1)
Pot B
(ADC 2)
Pot A
(ADC 3)
P10
P11
Servo 8
(Stand Servo)
Servo 1
(Stand Servo)
Servo 2
(Stand Servo)
Servo 3
(Stand Servo)
Servo 4
(Stand Servo)
Servo 5
(Stand Servo)
Servo 6
(Stand Servo)
Servo 7
(Stand Servo)
+5 to +6 VDC
Power Switch
(Position 1 or 2)
Servo
Power Supply
GND